Häfele: Officys table base system – individuality through diversity

The better office from the joiner

Top functionality, contemporary design and modern materials – the new Officys table base system from Häfele has all of this and much more. It can be configured individually thanks to its modular design, and can be assembled in no time. The versatile and creative system provides an attractive modular kit for the individual setting up of workplaces in modern offices.

The new table base for computer screen workstations features continuous, electric height adjustment, enabling work to be carried out either sitting or standing. With a 25 mm thick table top, the mere push of a button lifts or lowers the unit for heights between 620 and 1280 mm. Furthermore, the automatic, piezo-electric switch off function ensures safe operation. All of the parts are symmetrically constructed so that components can be flexibly laid out for right or left set-up.

Häfele’s table bases with their newly designed square columns are made of plastic coated steel and available in signal white, white aluminium or graphite black. Häfele has further expanded its range of accessories for these products. All of the accessories are fitted to the table base. The table top will always have the same drilling pattern. It can be produced very efficiently, irrespective of the configuration.

The pedestal also has a quick hook-in system and is fixed to the frame without the need for tools. At the back of the pedestal, storage space for cable management is available.

Compatible with the base for a computer screen workstation, Häfele also has a new table base with four legs, of the new generation, featuring square legs for multi-use units, for use with side or occasional tables or for use with meeting and conference tables.

The comprehensive range of accessories includes attractive felt screens for soundproofing and privacy, drawer organisation systems, socket strips and innovative felt drawers.

Further information is available from

Häfele GmbH & Co KG, Postfach 1237,

Nagold, Germany, Tel.: +49 7452 95-0,

Fax: +49 7452 95-200,

E-Mail: info@haefele.de

Captions:

250616_Fig1_Officys_table_bases.jpg

Thanks to the modular design, the new Officys table bases from Häfele are individually configurable to the extreme, and fitted in a flash.

250616_Fig2_Officys_table_bases.jpg

Drawer systems made easy, with original accessories for the Officys table base system from Häfele.

250616_Fig3_Officys_table_bases.jpg

Storage space on the back of the Officys pedestal, for cables or a small PC.

250616_Fig4_Officys_table_bases.jpg

The felt drawer brings a new look to the modern office

250616_Fig5_Officys_table_bases.jpg

The control unit for height adjustment on Häfele’s table base is integrated in the table top.

Photos: Häfele

Häfele is an internationally organized family owned and operated business with headquarters in Nagold, Germany. It was founded in 1923 and today serves the furniture industry, architects, planners, cabinet makers/joiners as well as dealers in over 150 countries around the world with furniture fittings and architectural hardware as well as electronic access control systems. Häfele develops and manufactures hardware fittings and electronic access control systems in 6 factories in Germany and Hungary. In the 2015 financial year the Häfele Group achieved exports of 79% with over 7,100 employees in 37 subsidiaries and numerous additional dealerships around the world and revenue of 1.3 billion Euros.